## Slide 1: Insole Design for Additive Manufacturing – Current Developments and Future Trends
Tatjana Spahiu1, Ioannis Ntintakis2, Ioannis Sarris3
1Polytechnic University of Tirana, Albania
2Hellenic Mediterranean University, Estavromenos, 714 10 Heraklion, Crete, Greece
3University of West Attica, 12244 Athens, Greece
SmartTecStyle conference 2024 11 – 12 December

## Slide 2: Content
SmartTecStyle conference 2024 11 – 12 December
Insoles – definitions, importance, history
Main materials used for production
Methods to design and manufacturing insoles
Smart insoles – a solution to monitor consumers
for different purposes
Current and future trends

## Slide 3: Definitions of insoles
SmartTecStyle conference 2024 11 – 12 December
Insoles are thin pieces inserted inside a shoe. They are the contact point between the foot or human body and the sole or the lower part of the shoes.

## Slide 4: Definitions of insoles
SmartTecStyle conference 2024 11 – 12 December
General word used for the piece that located inside of the shoe in contact with the foot.
It’s the part of the shoe that lies under the bottom of the foot.
Insoles are also often called foot beds.
Insoles are also referred to as shoe inserts.

## Slide 5: Definitions of insoles
SmartTecStyle conference 2024 11 – 12 December
The International Organization for Standardization defines an orthosis as “an externally applied device”.

## Slide 6: The role of insoles
SmartTecStyle conference 2024 11 – 12 December
Moisture control
Insoles
Attached
Movable
Comfort
Odor control
Reduce foot pain
Postural support
Foot orthoses or insoles have different applications depending on the type of shoe and modify the structural and functional characteristics of the neuromuscular and skeletal systems.

## Slide 7: Brief history of Insoles
SmartTecStyle conference 2024 11 – 12 December
Data found highlight the use of insoles since more then150 years ago.
1958 that the era of modern foot orthosis therapy began.
Podiatrist, Merton Root, began to fabricate thermoplastic foot orthoses

## Slide 8: Main materials for insole production
SmartTecStyle conference 2024 11 – 12 December
Thermoplastics
Source: Nicolopoulo, C.S. et al., Foot, 10, 1, 2000.
Acrylic
Carbon fiber composite
Foams
Leather
Cork
Spenco
Vinil

## Slide 9: Main materials for insole production Thermoplastics
SmartTecStyle conference 2024 11 – 12 December
Plastic that turns soft when heated and hard when cooled
Source: Nicolopoulo, C.S. et al., Foot, 10, 1, 2000.
Thermoplastics | Usage | Advantages | Disadvantages
Polypropylene | Shell material | lightweight, high stiffness | prone to cracking if notches or grooves are introduced
Polyethylene |  | durable, lightweight, flexible, malleable, and resilience to compression | limited shock absorption

## Slide 10: Main materials for insole production Acrylic Carbon fiber composite
SmartTecStyle conference 2024 11 – 12 December
methyl methacrylate polymer
Source: Nicolopoulo, C.S. et al., Foot, 10, 1, 2000.
Materials | Usage | Advantages | Disadvantages
Acrylic | Shell material | tough and remoldable | prone to cracking
Carbon fiber composite | Shell | thin, ultralight weight, rigid, extremely durable, and retains shape | difficult to cut and inability to remold
combination of acrylic plastic with carbon fibers

## Slide 11: Main materials for insole production Foams
SmartTecStyle conference 2024 11 – 12 December
cellular material classified as closed cell (isolated air pockets) or
open cell (porous air pockets) with varying densities, such as soft or firm
Source: Nicolopoulo, C.S. et al., Foot, 10, 1, 2000.
Types of foams | Usage | Advantages | Disadvantages
EVA (ethyl vinyl acetate) foam | topcover (soft), accommodations (firm), shell (firm) | shock absorption (soft), durable, resists tearing, rigid (firm), heat moldable | compressibility (soft), limited cushioning (firm)
Polyurethane foam | top layer, cushioning | high shock absorption, resists compression | durability as a top cover and not heat moldable
Polyethylene foam | top cover (soft), shell (firm) | tough, durable, malleable, lightweight, flexible, heat moldable | moderate shock attenuation, easily compressed

## Slide 12: Main materials for insole production
SmartTecStyle conference 2024 11 – 12 December
Leather, Cork, Spenco and Vinyl are all used for the top cover of the insole
Source: Nicolopoulo, C.S. et al., Foot, 10, 1, 2000.
Materials | Advantages | Disadvantages
Leather | low friction, durable, thin, tear resistant, absorbs moisture | no cushioning, remains damp, and stains
Cork | Lightweight | Durability
Spenco | Soft cushioning system to help absorb shock and reduce friction | Durability
Vinyl | tough, long-lasting, extremely thin, resists tearing, does not absorb moisture, minimal friction | No cushioning

## Slide 13: Insoles production
SmartTecStyle conference 2024 11 – 12 December
Mass-produced insoles
Custom-made insoles, or custom foot orthotics
Manufactured for basic needs
odor and moisture control,
arch support, or
extra-cushioning
Manufactured with extra features based on the specific needs of the individual

## Slide 14: Customized insoles based on traditional method
SmartTecStyle conference 2024 11 – 12 December
Orthotic insoles can be produced by starting with the footprint in a foam of box
Low precision
Low accuracy
Low comfort
High costs
Time consuming

## Slide 15
SmartTecStyle conference 2024 11 – 12 December
Advanced technologies for insoles production
Design and fabrication of custom insoles/foot orthoses
1
Capturing the geometry
2
Manufacturing
3
Design of the device
Personalized insoles are becoming a trend not only for fit and comfort but for aesthetical purposes too.

## Slide 16: Customized insoles based on digital twin
SmartTecStyle conference 2024 11 – 12 December
Kim, J., Choi, J., Kang, YJ. et al. Development of Customized Insole Design Framework Based on Digital Twin. Int. J. Precis. Eng. Manuf. 25, 785–798 (2024). https://doi.org/10.1007/s12541-023-00952-y
Studies propose a customized insole design framework for individual foot shapes by constructing a digital twin model between a finite element analysis (FEA)based virtual model and an actual physical model.
Foot pressure data from the physical model were used as a load condition for the FEA model, and the insole material properties were tuned to maximize the similarity between the FEA model and the real model using virtual sensors.
Results: The obtained digital twin model corrected the abnormal arch index of the cavus foot to normal through position optimization of the partial insole, and subsequently balanced the front and rear of the foot.

## Slide 17: 3D printing technology
SmartTecStyle conference 2024 11 – 12 December
The process works by laying down thin layers of material in the form of liquid or powdered plastic, metal or cement, and then fusing the layers together.
Three-dimensional (3D) printing is an additive manufacturing process that creates a physical object from a digital design.

## Slide 18: Advantages of 3D printed customized insoles
SmartTecStyle conference 2024 11 – 12 December
Breathability and Moisture Management
Enhanced Support and Cushioning
Cost-Effectiveness
Sustainability and Eco-Friendliness
Personalization and Custom Fit

## Slide 19
SmartTecStyle conference 2024 11 – 12 December
Advantages of 3D printed customized insoles
3D printing enables the creation of insoles according to foot shape, size, and gait.
It ensures optimal comfort and support, reducing the risk of foot pain and injuries.
3D printed insoles can be designed with complex structures and varying densities.
This provides custom support and cushioning.
Especially for people with specific foot conditions or high-impact activities.

## Slide 20
SmartTecStyle conference 2024 11 – 12 December
Advantages of 3D printed customized insoles
The materials used in 3D printing, such as nylon or TPU, allow for better breathability and moisture management.
This helps keep feet dry and comfortable, reducing the risk of blisters and other skin irritations.
3D printing reduces material waste and enables on-demand production, making it a more sustainable and eco-friendly option compared to traditional manufacturing methods.

## Slide 21
SmartTecStyle conference 2024 11 – 12 December
Advantages of 3D printed customized insoles
While the initial investment in 3D printing technology may be higher, the long-term cost savings are significant.
Custom insoles can be produced quickly and cheaply, without the need for expensive tooling or minimum order quantities.

## Slide 22: Smart products - insoles
SmartTecStyle conference 2024 11 – 12 December
A smart, or connected, product is a device that is linked to the Internet.
The data provided by smart products can be used to monitor and optimize usage,
Provide health status or location and
Predict/prevent failures by anticipating service needs.

## Slide 23: Smart products - insoles
SmartTecStyle conference 2024 11 – 12 December
Recognizing human activities in controlled and uncontrolled environments is an ongoing work of many researchers.
Analyze images or videos obtained from capture devices
Focus on processing data extracted from wearable/environmental
sensors
As smart shoes/insoles can detect data about humans, there are two main two main categories in terms of the devices used:
Vision-based HAR (Human Activity Recognition)
Sensor-based HAR
Human Activity Recognition)

## Slide 24: Insoles design for additive manufacturing
SmartTecStyle conference 2024 11 – 12 December

## Slide 25: Insoles design for additive manufacturing
SmartTecStyle conference 2024 11 – 12 December

## Slide 26: Conclusions
SmartTecStyle conference 2024 11 – 12 December
3D-printed orthotic insoles are becoming increasingly popular as a way to relieve foot pain and other conditions.
They are custom-made to fit the individual's foot and can be designed to address specific needs.
Compared to traditional way of capturing foot shapes and model forming processes, 3D scanning provides:
High accuracy
High capturing speed
Reduced manual labor
Flexibility
3D Scanning

## Slide 27: Conclusions
SmartTecStyle conference 2024 11 – 12 December
The U.S. shoe insoles market size was estimated at USD 1.06 billion in 2023 and is projected to grow at a CAGR of 5.1% from 2024 to 2030.
Rise in sports and physical activities
Significant effect on the market for shoe insoles
Driving up customer demand for personalized insoles
Comfort
Performance
Lower injury risks

## Slide 28: Conclusions
SmartTecStyle conference 2024 11 – 12 December
For rehabilitation medicine, traditional production technology can no longer fully meet the needs of patients.
3D printing technology has the advantages of individualization, which is small batches and high precision.
It can easily solve the problems of individual differences among patients and build a personalized health industry.
The gap between demand and production scale helps medical device manufacturers improve their production flexibility, also assisting doctors or researchers to bring better precision medicine solutions to patients.

## Slide 29: Conclusions
SmartTecStyle conference 2024 11 – 12 December
Smart insoles have the potential to become one of the top wearable’s soon

## Slide 30
SmartTecStyle conference 2024 11 – 12 December
THANK YOU!